## Slide 1
Centre for Economic Performance, 2010
Introduction to Lean and Modern Manufacturing Techniques
<number>
Notes: <number>

## Slide 2: AGENDA
<number>
  Introduction to lean and key principles
  Waste
  Variability
  Inflexibility
  Conclusion and questions
Notes: Identifier top left
<number>

## Slide 3: LEAN IMPROVEMENT SEEKS TO MINIMISE THE SOURCES OF LOSS: WASTE, VARIABILITY AND INFLEXIBILITY
<number>
Business flows
Performance indicators
Waste
Inflexibility
Variability
People
Process
Material
Information
Quality
Cost
Delivery
Business system
Sources of loss
Notes: Identifier top left
<number>

## Slide 4: MOST ORGANIZATIONS DRAW ON ONE OF THREE POPULAR APPROACHES TO IMPROVING THEIR OPERATIONS
<number>
Six Sigma
Lean
Theory of Constraints
Variability
Waste
Inflexibility
Notes: Identifier top left
<number>

## Slide 5: ‘LEAN’ IS THE ENGINE WHICH KEEPS TOYOTA IN FRONT
<number>
The Toyota Production System developed from the 1950s
  Pursues flow throughout the entire value stream by the elimination of waste
  Builds quality in at the manufacturing process, while recognizing the principle of cost reduction
It takes fewer man hours to make a Lexus from scratch than to re-work a German luxury car at the end of the production line – after it has been made
Notes: Identifier top left
<number>

## Slide 6: TOYOTA PERFORMS EXTRAORDINARILY WELL IN A TOUGH INDUSTRY
<number>
Market value, indexed 1975 = 1
"More than twenty years ago, we concluded that best of the best was Toyota.
In the years since we reached this conclusion, we’ve often wondered what would happen to the lean movement if Toyota faltered. Fortunately, we’ve never found out because Toyota has marched from victory to victory over the past twenty years while sharing its business system freely with the world.
In the mid-1990s, Toyota set a goal of a 10% market share in the global motor vehicle market by 2000 and in 2000 Toyota’s share was 10.01%. Last year Toyota announced a new vision to achieve a global motor vehicle market share of 15% by 2010, which will push Toyota past GM and Ford as the global market share leader.
This is not being done at the expense of profits, which have been rising steadily in step with growing market share.”
Jim Womack
Notes: Identifier top left
<number>

## Slide 7: THE TOYOTA PRODUCTION SYSTEM IS BASED ON STANDARDISED WORK
<number>
Toyota Production System (TPS) framework
Cost
reduction through flexible manning
Jidoka
Just In Time
Standardised work
Notes: Identifier top left
<number>

## Slide 8: THE TOYOTA PRODUCTION SYSTEM IS BASED ON STANDARDISED WORK
<number>
Toyota Production System (TPS) framework
Cost
reduction through flexible manning
Jidoka
Just In Time
Standardised work
Standardised work
Common work methods to ensure safety and quality
Jidoka
The principle of stopping a process immediately an abnormality occurs
Just In Time (J.I.T)
Linking production rate to customer demand
Flexible manning
Maintaining productivity despite demand fluctuations
=
=
=
=
  TPS has three desired outcomes
    To provide customers with the highest quality products, at lowest possible cost, in a timely manner with the shortest possible lead time
    To provide workers with job satisfaction, security and fair treatment
    To give the company flexibility to respond to the market, achieve profit through cost reduction activities and long-term prosperity
  Toyota have been developing their production system since 1948 and are recognised as global best practice. It strives for the absolute elimination of waste, overburden and unevenness to allow smooth and efficient work
Notes: Identifier top left
<number>

## Slide 9: JIT
Producing the right part in the right place at the right time…..
Stabilize and level the MPS with uniform plant
Reduce or eliminate setup
Reduce lot sizes
Reduce lead times
Preventive maintenance
Flexible work force
Require supplier quality assurance and implement a zero defects quality program
Small‑lot (single unit) conveyance (kanban)
Notes: Identifier top left
<number>

## Slide 10: BASICS OF LEAN OPERATIONS
<number>
Beliefs of lean
  Waste arises everywhere in a system from variability, redundancy, and inflexibility in how things are done
  Waste leads to poor service, quality, and financial outcomes
  Waste must be eliminated
What it is
  Lean operations is a framework of concepts and methods to achieve continual gains in productivity while satisfying customers’ expectations for service quality
What it is not
  Making people work harder or do the same with fewer people
  A short-term project
  Limited to manufacturing plants
  Mean!!
How to do it
  First, identify activities which add value vs. those which are waste
  Apply lean tools to reduce variability and redundancy in order to eliminate waste and improve service, quality, and cost
Notes: Identifier top left
<number>

## Slide 11: SIX SIGMA HAS THREE CLEAR ELEMENTS TO ITS APPROACH
<number>
3. Focuses on reduction in variation of key metrics
2. Drives measurement and data-driven analysis of metrics that are critical to customers
1. Creates standardized, disciplined problem solving approach used across company
  Define the problem
  Measure the problem
Define
Measure
Analyze
Improve
Control
  Analyze and identify the gap
  Identify and implement solutions
  Track and review progress
D
M
A
I
C
Prescriptive Problem Solving Process – “DMAIC”
1
  Brainstorming
  Affinity diagrams
  Multi-voting
  Hypothesis testing
  Pareto charts
  Fishbone
  Process mapping
Statistically-focused problem solving tools
  Root cause problem solving
  Design of experiment
  Voice of the customer
  Quality function deployment
  ANOVA
  Etc.
2
Master Black Belts (full time)
  Support key line executives
  Responsible for project selection, training/ coaching of Black Belts and reporting progress
Black Belts
(full time)
  Lead improvement projects through DMAIC cycle
  Receive 4 weeks of up-front training
Green belts
(part time)
  Provide Black Belts with support to get projects done
  Receive less intensive training
Dedicated and certified resources
3
All Six Sigma improvement efforts optimize processes by reducing variation
Notes: Identifier top left
<number>

## Slide 12: TOYOTA’S LEAN AND GE’S SIX SIGMA ARE DIFFERENT BUT HAVE SOME OVERLAP
<number>
Definition
. . . an integrated operating system of principles, practices, tools and techniques
. . . a structured improvement methodology using a standard approach and statistical tools
Lean
Six Sigma
Driving
principle
  Reduce waste
  Synchronize flows
  Manage variability
  Operational KPIs cascaded to front line
Performance
management
Lean experts
Team leaders
Natural teams
Infrastructure
& Involvement
  Systematic value stream mapping
  Current state and future state
Project
selection
Prescriptive solutions:
One piece flow
Pull System
SMED
Standardized work
Problem
solving
  Root cause analysis
  Process mapping
  Basic analytic tools
Reduce variation
  Project metrics
Black belts, MBBs, GBs
Six Sigma project support
Ad hoc teams
  Driven by key issues and problems in current processes
Prescriptive processes:
DMAIC
DMADV/DFSS
Statistical approaches
DOE
Gauge R&R
Notes: Identifier top left
<number>

## Slide 13: THEORY OF CONSTRAINTS OFFERS STRATEGIES FOR DEALING WITH CONSTRAINTS
SCOUT GROUP EXAMPLE
<number>
“Herbie”
Move the constraint o the front
“Herbie”
Source: “The Goal” by Eliyahu M. Goldratt and Jeff Cox
X
Reduce the load on the constraint
Notes: Identifier top left
<number>

## Slide 14
<number>
THERE ARE ALSO SEVERAL CONFLICTS BETWEEN APPROACHES – NONE OF THE POINTS OF VIEW ARE “WRONG”, BUT THE CORRECT APPROACH SHOULD DEPEND ON THE CURRENT BUSINESS NEED
  Reduces Variation using statistical tools and SPC
  Identifies and delivers on customer requirements
  Driven through projects with strong links to business needs
6-Sigma
  Identifies bottlenecks / constraints and focuses a business around managing and eliminating these above all else
  Suggests build-to-order, with Just-In-Time delivery, to eliminate overproduction, reduce inventory, and improve service
Theory of Constraints (TOC)
  Shop-floor workshops, primarily aimed at reducing waste
  Involves everyone in change from the very start
  Quickly addresses key day-to-day frustrations of the shop floor
Kaizen Lean
Core ‘essence’ of Approach
6-sigma & lean
minimise variation
TOC builds contingency around Variation *
6 sigma uses very high-calibre experts (top 1%) for implementation
Lean encourages everyone to participate in continuous improvement
Example conflicts
* Often necessary at an early stage to gain control and stability. As variability is reduced the contingency can also be reduced
Notes: Identifier top left
<number>

## Slide 15: AGENDA
<number>
  Introduction
  Waste
  Variability
  Inflexibility
Notes: Identifier top left
<number>

## Slide 16: SEVEN + ONE TYPES OF WASTE
<number>
Materials or resources beyond what is needed to satisfy the customer
Overproduction
Transportation
Waiting
Inventory
Over-processing
Motion
Rework
8
Wasted intellect
Notes: Identifier top left
<number>

## Slide 17: WASTE EXAMPLES
<number>
8
Motion
Walking around the ward looking for something or fetching equipment
Inventory
Excess stock of drugs or equipment in clinical areas
Waiting
Clinical staff arriving late for theatre
Rework
Documenting the same information in several places for a new patient
Over-processing
Completing documentation which nobody will read
Over-production
Carrying out ‘standard’ tests on every patient regardless of need
Intellect
Failure to make full use of the whole team’s experience and knowledge
Transportation
Moving patients around the hospital
Notes: Identifier top left
<number>

## Slide 18: WASTE IS WORK WHICH ADDS COST, BUT DOESN’T ADD VALUE
<number>
Waste
Incidental Activity
Value Added Activity
Value Added Activity
  Work that directly increases the value of the product in the eyes of the customer (e.g. Assembly of parts)
  What the customer is paying for
Waste
  Work or use of resources that does not add any value to a product
  Waste is sometimes called "muda", from the Japanese for waste
Incidental Activity
  Work that does not directly add customer value, but which is currently necessary to maintain operations (e.g. small movements to reach for material for assembly)
Objective
The objective is to maximize the proportion of value added activity by eliminating waste and incidental activity
Elements of work
Notes: Identifier top left
<number>

## Slide 19: OUR OBJECTIVE IS TO REDUCE WASTE AND INCREASE THE % VALUE ADDED, IN ORDER TO REDUCE COST
<number>
Waste
Value Added Activity
Incidental Activity
Elements of Work
Notes: Identifier top left
<number>

## Slide 20: SPOT THE WASTE
<number>
Notes: Identifier top left
<number>

## Slide 21: SPOT THE WASTE
<number>
Notes: Identifier top left
<number>

## Slide 22: CONTINUOUS FLOW PROCESSING
<number>
Continuous Flow Processing is the first step in improving material flow
Process
3
Process
1
Process
2
Process
3
Process
1
Process
2
Traditional Manufacturing inhibits material flow and creates WIP
Notes: Identifier top left
<number>
Theory slide to support the practical learning.

## Slide 23: AGENDA
<number>
  Introduction
  Waste
  Variability
  Inflexibility
Notes: Identifier top left
<number>

## Slide 24: VARIABILITY CAN BE CONSIDERED AS HAVING 5 ‘SOURCES’ – WHICH ARE MOST RELEVANT TO YOUR ENVIRONMENT?
<number>
People
Materials
Process
Information
Quality
Delivery
Environment
Notes: Identifier top left
<number>
The logo for this is deliberately chosen as a “fishbone diagram”, as this is often used when brainstorming possible root causes of variability.

## Slide 25: PEOPLE VARIABILITY IS CAUSED BY ISSUES SUCH AS ATTENDANCE AND SKILL
<number>
Attendance
Number absent
M
M
T
T
W
Th
F
W
Th
F
1
2
Average number absent
Absence Cover Level
Absence cover is 2 people per day, average of 1 person per day wasted
Skill
Number of defects/day
M
M
T
T
W
Th
F
W
Th
F
0
5
10
15
A
B
Operator A creates more rework than operator B
Use flexible working to cover absence, and standardised work to reduce variability caused by skill level gaps
Action
Notes: Identifier top left
<number>

## Slide 26: PROCESS VARIABILITY IS CAUSED BY OPERATOR METHOD AND MACHINE ISSUES
<number>
% OEE
Variation of operator work content
20
40
60
80
100
M
M
T
T
W
Th
F
W
Th
F
Machine reliability
A
B
Work content
C
Product
Variable OEE can mean that expensive extra capacity is needed, just to deal with the ‘bad days’
Different products have different work contents – Either level or find ways to equalise the Work Content
Use root cause analysis, 6-sigma tools, standardised work, kaizen and levelling to under-stand and attack the causes of process variability
Action
Notes: Identifier top left
<number>

## Slide 27: EXAMPLE OF A SIMPLE TOOL – STANDARDISED WORK
<number>
Before – 3 ways to deburr hole
After – one way
  Different methods for same basic task across shifts and operators
  Best practice now standardized and documented at workstation
    Improves quality
    Faster training
    Document becomes foundation for continuous improvement
Notes: Identifier top left
<number>

## Slide 28: MATERIAL VARIABILITY IS CAUSED BY QUALITY AND DELIVERY TIME OF MATERIAL ARRIVING AT A PROCESS
<number>
Process yield vs. raw material properties
Raw material
part thickness (mm)
Scrap rate, %
Delivery times
Mon
10.00
Tue
08.00
Wed
12.00
Thu
10.00
Mon
10.00
Fri
12.00
6 hrs
12 hrs
6 hrs
6 hrs
10 hrs
Daily delivery time
Working time between deliveries
10%
1.0
1.1
1.2
1.3
5%
Variability of incoming material may affect scrap rates in a process
Variable delivery times mean more stock has to be held
Set and enforce clear standards for suppliers on the quality and delivery standards expected of them
Action
Notes: Identifier top left
<number>
Note that “suppliers” in this sense includes internal processes that act as suppliers to downstream processes, not just external suppliers

## Slide 29: INFORMATION VARIABILITY IS CAUSED BY THE QUALITY AND RELEASE TIMING OF INFORMATION
<number>
Week | Order release time
30 | Wednesday 16:00
31 | Wednesday 20:00
32 | Thursday 10:00
33 | Wednesday 16:00
Inaccurate forecasts may lead to shortfall of raw materials for Product A and surplus for Product B
Release of orders
Forecast
orders
Actual
orders
Volume
Product B
Product A
Quality
Late order release to shop floor in week 32 causes production problems/line stops
Standardise and simplify the information collection and formatting. Have a reactive (flexible) process that does not heavily rely on accurate forecasts
Action
Notes: Identifier top left
<number>

## Slide 30: ENVIRONMENT VARIABILITY COVERS THINGS SUCH AS CHANGES IN TEMPERATURE, HUMIDITY ETC., WHICH CAN AFFECT THE PROCESS
<number>
Extremes of temperature or humidity might affect the yield of the process
Winter conditions might make the workplace hazardous
Rain might damage electronics (particularly if the roof is leaking)
Protect the process from changes in the environment, or make the process resilient to them
Action
Notes: Identifier top left
<number>
A good example of environmental factors being important is in microprocessor production, where manufacturers use rooms with constant temperature and humidity all the time. This is because experience has shown that changes in environmental conditions can cause large changes in yields.

## Slide 31: VARIABILITY INCREASES ‘COST’ BECAUSE OF CONTINGENCY PLANS FOR POOR QUALITY AND UNRELIABLE DELIVERY
<number>
Cost
Variable delivery
  Requires making product early
  Requires additional resources
Variable quality
  Adds rework
  Increases scrap
With contingencies
Without contingencies
Notes: Identifier top left
<number>

## Slide 32: VARIABILITY IS A CONCERN WHEN THE PROCESS RANGE IS WIDER THAN THE ACCEPTABLE RANGE
<number>
Voice of the process
Voice of the customer
Voice of the process
Voice of the customer


Notes: Identifier top left
<number>

## Slide 33: AGENDA
<number>
  Introduction
  Waste
  Variability
  Inflexibility
Notes: Identifier top left
<number>

## Slide 34: INFLEXIBILITY ADDS COSTS TO MEET EXACT CUSTOMER NEEDS OR TO MEET DELIVERY/PRODUCT REQUIREMENTS
<number>
Mix
Product
Volume
Delivery
Inability to flex overall output levels (e.g., for seasonal demand changes)
Inability to change between products to meet changing customer demand
Inability to deliver to the exact lead times the customer wants
Inability to provide the product or service the customer wants (e.g., limited configurations)
Notes: Identifier top left
<number>

## Slide 35: AGENDA
<number>
  Introduction to lean and key principles
  Waste
  Variability
  Inflexibility
  Conclusion and questions
Notes: Identifier top left
<number>

## Slide 36: LEAN MANUFACTURING IS A COMPREHENSIVE TERM REFERRING TO MANUFACTURING METHODOLOGIES BASED ON MAXIMISING VALUE AND MINIMISING WASTE IN THE MANUFACTURING PROCESS
Key principles of lean include the following:
  5S
  Total Productive Maintenance (TPM)
  Takt time
  Six Sigma
  Kaisen Philosophy
  Andon, Plant Floor Displays and Area/Line Communications
  Value Steam Mapping (VSM)
  Quick Change Over or Single Minute Exchange of Die (SMED)
<number>
Notes: Identifier top left
<number>

## Slide 37
  5S
    Sift, sort, sweep sustain and self-discipline
  Total Productive Maintenance (TPM)
    Zero breakdown
    Zero defects
  Takt time
    Max time allowed to produce in order to meet demand
  Six Sigma
    Data driven problem solving
    Define, Measure, Analyse, Improve, Control
<number>
LEAN MANUFACTURING IS A COMPREHENSIVE TERM REFERRING TO MANUFACTURING METHODOLOGIES BASED ON MAXIMISING VALUE AND MINIMISING WASTE IN THE MANUFACTURING PROCESS
Notes: Identifier top left
<number>

## Slide 38: LEAN MANUFACTURING IS A COMPREHENSIVE TERM REFERRING TO MANUFACTURING METHODOLOGIES BASED ON MAXIMISING VALUE AND MINIMISING WASTE IN THE MANUFACTURING PROCESS
  Kaisen Philosophy
    Continuous improvement
    Look for managers referring to Kaisen events
  Andon, Plant Floor Displays and Area/Line Communications
    Visual management tool
    E.g. – lights on machines to indicate status
  Value Steam Mapping (VSM)
      Map entire process from concept to end delivery
      Note value of every stage
  Quick Change Over or Single Minute Exchange of Die (SMED)
    SMED (Single Minute Exchange of Dies)
    Attempts to reduce output and quality losses due to changeovers
<number>
Notes: Identifier top left
<number>

## Slide 39: TAKEWAYS: CORE PRINCIPLES OF LEAN
Create value streams
Flow the value along the stream
Pull products at the points where flow must be broken
Flex the operation to match customer demand
Introduce information defining customer requirements at a single point
Standardise operations to create a foundation for flexibility
Detect and fix abnormalities as close as possible to the point where they occur
Watch jargon!!
Notes: Identifier top left
<number>

## Slide 40: QUESTIONS?
Notes: Identifier top left
<number>

## Slide 41: BACKUP
Notes: Identifier top left
<number>

## Slide 42: DEFINITIONS
Kanban: “pull” production control system uses simple, visual signals to control the movement of materials between work centres as well as the production of new materials to replenish those sent downstream to the next work centre
Flexible work force: workers should be trained to operate several machines, to perform maintenance tasks, and to perform quality inspections; teams of competent, empowered employees who have more responsibility for their own work.
  The Toyota Production System concept of “respect for people” contributes to a good relationship between workers and management.
Notes: Identifier top left
<number>

## Slide 43: EXAMPLE OF A TECHNIQUE – WORK BALANCING TO TAKT TIME
<number>
Future (Continuous flow) state
Current state
Target Manpower = Total Cycle Time
Takt time
1 2 3 4 5
time
Operator
19
21
16
33
27
43 minutes
43 minutes
30 minutes
116 minutes
5
4
3
1
2



c/t
time
Operator
43
30
takt
43



Work Rebalancing
Notes: Identifier top left
<number>
This is a backup slide, for use if it is necessary to discuss work balance. Most participants will be familiar with it from the JIT/crane game.

## Slide 44: EXAMPLE OF A TECHNIQUE –AUTONOMATION (‘JIDOKA’)
<number>
  Built-in quality control at each process
    Line-stop concept
    Standard work instructions
  Quality feedback on cause of error is immediate
  Similar errors are not seen repeatedly
Inspect
Scrap
Redo
Ship
C
B
A
  100% final inspection
  No quality feedback to operators on defects
  Extra rework operations required
  High cost, since defects are detected at higher value-added level
Ship
C
B
A
Eliminate costly rework and drives up worker respon-sibility for quality
Traditional production method . . .
. . . lean control (“Poka Yoke – I will not accept, make or pass defects”)
Notes: Identifier top left
<number>

## Slide 45: INFLEXIBILITY OF STAFFING EXACERBATED BY BRANCH HABITS
<number>
Fax demand
Current schedule capacity
Number of applications sent by the branches
Before the transformation
0
20
40
60
80
100
120
140
7
AM
8
9
10
11
12
1
PM
2
3
4
5
6
7
8
9
10
11
After the transformation
Branches send applications
in small batches
0
20
40
60
80
100
120
140
7
AM
8
9
10
11
12
1
PM
2
3
4
5
6
7
8
9
10
11
Branches send batches before lunch break
Branches send batches after closure
Underwriters are asked to adopt flexible schedules
Notes: Identifier top left
<number>

## Slide 46: ALL CAN BE CONSIDERED SYNCHRONOUS MANUFACTURING, BUT THERE ARE SEVERAL KEY DIFFERENCES BETWEEN APPROACHES
NONE OF THE POINTS OF VIEW ARE “WRONG”, BUT THE CORRECT APPROACH SHOULD DEPEND ON THE CURRENT BUSINESS NEED
Lean is implicit in its treatment of constraints, or the slowest step, TOC is explicit:-
  Raw material release, points of convergence/divergence, constraint and shipping need to be tied together
  Mechanism to do so is a time-phased schedule
TOC (drum-buffer-rope) can operate at any product volume or level of diversity
Notes: Identifier top left
<number>